## Slide 1: Internet Of Things (IoT) Advanced
Raghu Prasad
9845547471
www.kaushalya.tech
FB : https://www.facebook.com/raghuprasadkonandur/
Skill Up-Skill Re-Skill
Excellence in action

## Slide 2: Introduction
Raghu Prasad – BE, MS
Total of 24 years of experience
7 years as a lecturer in an Engineering College
17 Years into IT
Worked with companies like CISCO,CSC,ICICI,First Apex – NTT Data
Currently into Corporate training and consultancy
Worked with corporates and public sector
Service Offerings – In person/On-line/Corporate/Academic Institutes
Technologies – Java,Python,Web technologies,Java Script technologies (MEAN stack),IOT,Test Automation,Machine Learning,Artificial Intelligence,ERP
Customers – L & T,NextGen,Incarnus,BGS-IT,Sindhi College

## Slide 3: Topics
Communication protocols – Deep dive
Cloud Computing
IoT Platforms
IoT Consortiums
AWS IoT Deep dive
Data analysis
Design Considerations and IoT Security
IoT Opportunities
Demonstration

## Slide 4: Communication Protocol – MQTT – Deepdive
What is MQTT?
MQTT stands for MQ Telemetry Transport. It is a publish/subscribe, extremely simple and lightweight messaging protocol, designed for constrained devices and low-bandwidth, high-latency or unreliable networks. The design principles are to minimise network bandwidth and device resource requirements whilst also attempting to ensure reliability and some degree of assurance of delivery. These principles also turn out to make the protocol ideal of the emerging “machine-to-machine” (M2M) or “Internet of Things” world of connected devices, and for mobile applications where bandwidth and battery power are at a premium.
Who invented MQTT?
MQTT was invented by Dr Andy Stanford-Clark of IBM, and Arlen Nipper of Arcom (now Eurotech), in 1999.
Where is MQTT in use?
MQTT has been widely implemented across a variety of industries since 1999.
Is MQTT a standard?
As of March 2013, MQTT is in the process of undergoing standardisation at OASIS.
The protocol specification has been openly published with a royalty-free license for many years, and companies such as Eurotech (formerly known as Arcom) have implemented the protocol in their products.
In November 2011 IBM and Eurotech announced their joint participation in the Eclipse M2M Industry Working Group and donation of MQTT code to the proposed Eclipse Paho project.

## Slide 5: Communication Protocol – MQTT – Deepdive
How does MQTT relate to SCADA protocol and MQIsdp?
The “SCADA protocol” and the “MQ Integrator SCADA Device Protocol” (MQIsdp) are both old names for what is now known as the MQ Telemetry Transport (MQTT). The protocol has also been known as “WebSphere MQTT” (WMQTT), though that name is also no longer used.
What is WebSphere MQ Telemetry?
This is a product from IBM which implements the MQTT protocol in a very scalable manner and which interoperates directly with the WebSphere MQ family of products.
Are there standard ports for MQTT to use?
Yes. TCP/IP port 1883 is reserved with IANA for use with MQTT. TCP/IP port 8883 is also registered, for using MQTT over SSL.
Does MQTT support security?
You can pass a user name and password with an MQTT packet in V3.1 of the protocol. Encryption across the network can be handled with SSL, independently of the MQTT protocol itself (it is worth noting that SSL is not the lightest of protocols, and does add significant network overhead). Additional security can be added by an application encrypting data that it sends and receives, but this is not something built-in to the protocol, in order to keep it simple and lightweight.
Notable MQTT projects
http://mqtt.org/projects

## Slide 6: MQTT – Terminologies
Terminology

## Slide 7: MQTT – Terminologies
Terminology

## Slide 8: MQTT – Terminologies
Terminology (http://www.steves-internet-guide.com/mqtt-protocol-messages-overview/)

## Slide 9: MQTT – Terminologies
Terminology

## Slide 10: MQTT – Terminologies
Terminology

## Slide 11: MQTT - Demo
Broker
  M2M Eclipse(m2m.eclipse.org)
  Mosquitto (https://mosquitto.org/)
  Mosquitto installed on the laptop
  Client
  MQTT.fx (Web client)
  MyMQTT (Android client)
  MQTTLens(Chrome Extension)

## Slide 12: MQTT – Demo – Scenario 1
Broker – Mosquitto installed on system
  Client - Mosquitto installed on system (Publisher and Subscriber)
  Steps
    Download mosquitto (https://mosquitto.org/download/)
    Install mosquito
    Start mosquitto as a windows service
    Publish and Subscribe

## Slide 13: MQTT – Demo – Scenario 1

## Slide 14: MQTT – Demo – Scenario 1

## Slide 15: MQTT – Demo – Scenario 1
To check running of mosquitto on port 1883
  netstat -an | findstr 1883
Publish message
  mosquitto_pub -h "192.168.43.136" -t test -m "hi"
Subscribe to message
  mosquitto_sub -h "192.168.43.136" -t test

## Slide 16: MQTT – Demo – Scenario 2
Broker – Mosquitto on local system
  Client - MQTT.fx (Web client) (Download - http://mqttfx.jensd.de/index.php/download http://mqttfx.jensd.de/index.php/download

## Slide 17: MQTT – Demo – Scenario 3
Broker – Mosquitto on local system
  Client –MyMQTT (Android App)

## Slide 18: MQTT – Demo – Scenario 4
Broker - http://test.mosquitto.org/
  Client - MQTT.fx (Web client) (usage of # and +)

## Slide 19: Raspberry pi
https://www.raspberrypi.org/
  The Raspberry Pi is a series of small single-board computers developed in the United Kingdom by the Raspberry Pi Foundation to promote the teaching of basic computer science in schools and in developing countries.The original model became far more popular than anticipated,selling outside its target market for uses such as robotics. It does not include peripherals (such as keyboards, mice and cases). However, some accessories have been included in several official and unofficial bundles.
  According to the Raspberry Pi Foundation, over 5 million Raspberry Pis were sold by February 2015, making it the best-selling British computer.By November 2016 they had sold 11 million units and 12.5m by March 2017, making it the third best-selling "general purpose computer".In July 2017, sales reached nearly 15 million.

## Slide 20: Raspberry pi

## Slide 21: Projects on Raspberry pi
http://www.trustedreviews.com/opinion/best-raspberry-pi-projects-pi-3-pi-zero-2949390
An Amazon Alexa-powered dash cam
An electric skateboard
A disposable GIF camera
An electronic chess board
A Kodi media centre
A DIY NES Classic Mini
A digital DJ system
Automated entrance music
A robot arm
Multiroom audio for under £100
A walkie-talkie
A film-to-digital transfer system
A tiny retro games console
A magic mirror
A mini retro Macintosh Read more at http://www.trustedreviews.com/opinion/best-raspberry-pi-projects-pi-3-pi-zero-2949390#WlFlr3fl5UFfl88j.99

## Slide 22: Cloud Computing
Cloud computing is an information technology paradigm that enables access to shared pools of configurable system resources and higher-level services that can be rapidly provisioned with minimal management effort, often over the Internet
In other words it is use of remote servers on the internet to store, manage and process data rather than a local server or your personal computer.
Cloud computing relies on sharing of resources to achieve coherence and economies of scale, similar to a public utility.

## Slide 23: Cloud Computing

## Slide 24: Cloud Models
Cloud Models is of two types namely
Service Models
  Infrastructure As A Service (IaaS )
  Platform As A Service (PaaS)
  Software As A Service (SaaS)
Deployment Models
  Public Cloud
  Community Cloud
  Hybrid Cloud
  Private Cloud

## Slide 25: Cloud Models

## Slide 26: Cloud Models

## Slide 27: Cloud Models

## Slide 28: Cloud Market share

## Slide 29: Cloud Market share - SaaS

## Slide 30: Amazon Web Services (AWS)

## Slide 31: Amazon Web Services (AWS) https://aws.amazon.com/free/

## Slide 32: Amazon Web Services (AWS)

## Slide 33: Amazon Web Services (AWS)

## Slide 34: AWS-Getting started
Sign up using https://aws.amazon.com/
https://www.youtube.com/watch?v=ubCNZRNjhyo
Login

## Slide 35: AWS-Getting started
Click EC2->Launch Instance

## Slide 36: AWS-Getting started
Click EC2->Launch Instance->amazon Linux

## Slide 37: AWS-Getting started
Click EC2->Launch Instance

## Slide 38: AWS-Getting started
Click EC2->Launch Instance

## Slide 39: AWS-Getting started
Click EC2->Launch Instance

## Slide 40: AWS-Getting started
Click EC2->Launch Instance

## Slide 41: AWS-Getting started
Click EC2->Launch Instance

## Slide 42: AWS-Connect using SSH
https://docs.aws.amazon.com/AWSEC2/latest/UserGuide/putty.html?icmpid=docs_ec2_console

## Slide 43: What is an IoT platform ?
A platform is software and hardware, which may include an operating environment, storage, computing power, security, development tools, and many other common functions.
Platforms are designed to support many smaller application programs that actually solve business problems
Platforms are helpful because they abstract a lot of common functions away from the specific application logic
A good platform dramatically reduces the cost of developing and maintaining applications.
In the Internet of Things, platforms are designed to deploy applications that monitor, manage, and control connected devices. It stores the data securely and run analytics to make sense out of the data.
The IoT platforms are suites of components those help to setup and manage the internet connected devices. A person can remotely collect data, monitor and manage all internet connected devices from a single system. There are a bunch of IoT platforms available online but building an IoT solution for a company is all depend on IoT platform host and support quality
IoT platforms must handle problems like connecting and extracting data from a potentially vast number and variety of endpoints, which are sometimes in inconvenient locations with spotty connectivity.

## Slide 44: Key components of an IoT platform

## Slide 45: Key components of an IoT platform

## Slide 46: How to choose an IoT platform

## Slide 47: How to choose an IoT platform

## Slide 48: Prominent commercial IoT platforms
Amazon Web Services (AWS) IoT
Microsoft Azure IoT
Google Cloud Platform
ThingWorx IoT Platform
IBM Watson
Samsung Artik
Cisco IoT Cloud Connect
HPE Universal of Things (IoT) Platform
Salesforce IoT Cloud
Mindsphere by Siemens
Bosch IoT Suite
Carriots
Oracle Integrated Cloud
General Electric’s Predix

## Slide 49: Comparison of few commercial IoT platforms

## Slide 50: Prominent commercial IoT platforms
Amazon Web Services (AWS) IoT
Key Features
Registry for recognizing devices
Software Development Kit for devices
Device Shadows
Secure Device Gateway
Rules engine for inbound message evaluation
Easy facility for developers to connect sensors for multiple applications ranging from automobiles to turbines to smart home light bulbs.
Amazon has partnered with hardware manufacturers like Intel, Texas Instruments, Broadcom and Qualcomm to create starter kits compatible with their platform.

## Slide 51: IoT platforms – AWS IoT
IoT Services
AWS IoT Core
AWS IoT Device Management
WS IoT Analytics
AWS IoT Button

## Slide 52: IoT platforms – AWS IoT
IoT Services
AWS IoT Core
AWS IoT Core is a managed cloud platform that lets connected devices easily and securely interact with cloud applications and other devices. AWS IoT Core can support billions of devices and trillions of messages, and can process and route those messages to AWS endpoints and to other devices reliably and securely. With AWS IoT Core, your applications can keep track of and communicate with all your devices, all the time, even when they aren’t connected.

## Slide 53: IoT platforms – AWS IoT

## Slide 54: IoT platforms – AWS IoT
IoT Services

## Slide 55: IoT platforms – AWS IoT
IoT Services

## Slide 56: IoT platforms – ThingWorx
Thingworx is a platform for the rapid development and deployment of smart, connected devices. Its set of integrated IoT development tools support connectivity, analysis, production, and other aspects of IoT development.
Components
Thingworx offers several key tools for building applications. These tools include the Composer, the Mashup Builder, storage, a search engine, collaboration, and connectivity. The Composer provides a modeling environment for design testing. The Mashup Builder delivers easy dashboard building through common components (or widgets); for example, buttons, lists, wikis, gauges, and etc.
Thingworx uses a search engine known as SQUEAL, meaning Search, Query, and Analysis. Users employ SQUEAL in analyzing and filtering data, and searching records.

## Slide 57: IoT platforms – Thingworx

## Slide 58: IoT platforms – ThingWorx

## Slide 59: IoT platforms – Thingworx
Thingworx is a platform for the rapid development and deployment of smart, connected devices. Its set of integrated IoT development tools support connectivity, analysis, production, and other aspects of IoT development.
Components
Thingworx offers several key tools for building applications. These tools include the Composer, the Mashup Builder, storage, a search engine, collaboration, and connectivity. The Composer provides a modeling environment for design testing. The Mashup Builder delivers easy dashboard building through common components (or widgets); for example, buttons, lists, wikis, gauges, and etc.
Thingworx uses a search engine known as SQUEAL, meaning Search, Query, and Analysis. Users employ SQUEAL in analyzing and filtering data, and searching records.

## Slide 60: Prominent opensource IoT platforms
Kaa IoT Platform
SiteWhere
ThingSpeak
DeviceHive
Zetta
DSA
ThingsBoard
Thinger.io
WSO2

## Slide 61: Comparison of opensource platforms
IoT Software Platform | Device management? | Integration | Security | Protocols for data collection | Analytics | Support for visualizations? | DB
Kaa IoT Platform | Yes | Portable SDK available to integate any particular platfrom, REST API | Link Encryption (SSL), RSA key 2048 bits, AES key 256 bits | MQTT, CoAP, XMPP, TCP, HTTP | Real time IoT Data Analytics and Visualization with Kaa, Apache Cassandra and Apache Zappelin | Yes | MongoDB, Cassandra, Hadoop, Oracle NoSQL
SiteWhere | Yes | REST API, Mule AnyPoint, and more | Link Encryption (SSL), Spring Security | MQTT, AMQP, Stomp, WebSockets, and direct socket connections | Real-time analytics (Apache Spark) | No | MongoDB, HBase , InfluxDB
ThingSpeak | No | REST and MQTT APIs | Basic Authentication | HTTP | MATLAB Analytics | No | MySQL
DeviceHive | *Unknown | REST AP, MQTT APIs | Basic Authentication using JSON Web Tokens (JWT) | REST API, WebSockets or MQTT | Real-time analytics (Apache Spark) | Yes | PostgreSQL ,SAP Hana DB
Zetta | No | REST APIs | Basic Authentication | HTTP | Using Splunk | No | Unknown
Distributed Services Architecture (DSA) | NO | REST APIs | Basic Authentication | HTTP | No | No | ETSDB – Embedded Time Series
Thingsboard.io | Yes | REST APIs | Basic Authentication | MQTT, CoAP and HTTP | Real time analytics(Apache Spark, Kafka) | No | Cassandra
Thinger.io | Yes | REST APIs | Link Encryption (SSL/TLS) and basic authentication | MQTT, CoAP and HTTP | Yes | No | MongodB
WSo2 | Yes | REST APIs | Link Encryption (SSL) and basic authentication | HTTP, WSO2 ESB, MQTT | Yes, WSO2 Data Analytics Server | Yes | Oracle, PostgreSQL, MySQL, or MS SQL

## Slide 62: IoT Consortiums
As vendors struggle to make sense of the Internet of Things, many are realizing the need for consistent standards and broad interoperability for a seamless, connected ecosystem around IoT
Over the past few years, industry titans such as Intel and Cisco Systems have come together to form alliances and consortiums around the various components of the Internet of Things – including communications and broadband, connected buildings, connected home and industrial IoT.

## Slide 63: IoT Consortiums

## Slide 64: IoT Consortiums
The Industrial Internet Consortium was founded by Intel, IBM, GE, Cisco and AT&T in 2014.
This consortium aims to set the architectural framework for industrial IoT by coordinating various ecosystem initiatives to connect objects using common architectures, interoperability and open standards – making it easier to adopt interconnected machines and intelligent analytics.
Who It Impacts: Solution providers and systems integrators that want to build Internet of Things practices in the industrial space.
IEEE
The IEEE IoT Initiative was launched in 2014 by IEEE Future Directions and aims to help engineering and technology professionals learn, share knowledge and collaborate around IoT.
IEEE has a variety of programs that can help solution providers that are trying to understand IoT, including the IEEE Technical Community, which is made up of members involved in research, application and implementation of IoT
Who It Impacts: Solution providers that would like to better understand how to monetize the Internet of Things and are looking for real-life applications.

## Slide 65: AWS IoT – Deep dive
IAM – Manage User Access and Encryption Keys

## Slide 66: AWS IoT – Deep dive
Users – Add User

## Slide 67: AWS IoT – Deep dive
Add User

## Slide 68: AWS IoT – Deep dive
Groups

## Slide 69: AWS IoT – Deep dive
Groups

## Slide 70: AWS IoT – Deep dive
Groups

## Slide 71: AWS IoT – Deep dive
Groups

## Slide 72: AWS IoT – Deep dive
Groups

## Slide 73: AWS IoT – Deep dive
AWS-Iot

## Slide 74: AWS IoT – Deep dive
AWS-Iot-secure-certificates-create

## Slide 75: AWS IoT – Deep dive
Create a certificate – One click

## Slide 76: AWS IoT – Deep dive
Create a certificate – Download certificate - Activate

## Slide 77: AWS IoT – Deep dive
Create a certificate – Download certificate – Attach a policy

## Slide 78: AWS IoT – Deep dive
Create a certificate – Download certificate – create new policy

## Slide 79: AWS IoT – Deep dive
Advance mode

## Slide 80: AWS IoT – Deep dive
Add Statement

## Slide 81: AWS IoT – Deep dive
Add Statement

## Slide 82: AWS IoT – Deep dive
Policy created

## Slide 83: AWS IoT – Deep dive
Activate certificate

## Slide 84: AWS IoT – Deep dive
Attach policy

## Slide 85: AWS IoT – Deep dive
Attach policy

## Slide 86: AWS IoT – Deep dive
Certificate is active

## Slide 87: AWS IoT – MQTT.fx
Broker End point

## Slide 88: AWS IoT – Deep dive
MQTT.fx

## Slide 89: AWS IoT – Deep dive
AWS – IoT - Subscribe

## Slide 90: AWS IoT – Deep dive
MQTT-Publish

## Slide 91: AWS IoT – Deep dive
AWS - IoT

## Slide 92: AWS IoT – Actions
Actions- SNS Action

## Slide 93: AWS IoT – Actions
Actions- SNS Action

## Slide 94: AWS IoT – Actions
Actions- SNS Action

## Slide 95: AWS IoT – Actions
Actions- SNS Action

## Slide 96: AWS IoT – Actions
Actions- SNS Action

## Slide 97: AWS IoT – Actions
Actions- SNS Action

## Slide 98: AWS IoT – Actions
Actions- SNS Action

## Slide 99: AWS IoT – Actions
Actions- SNS Action

## Slide 100: AWS IoT – Actions
Actions- SNS Action

## Slide 101: AWS IoT – Actions – E-Mail
Act->Create a rule

## Slide 102: AWS IoT – Actions – E-Mail
Act->Create a rule

## Slide 103: AWS IoT – Actions – E-Mail
Act->Create a rule

## Slide 104: AWS IoT – Actions – E-Mail
SNS push notification

## Slide 105: AWS IoT – Actions – E-Mail
New resource

## Slide 106: AWS IoT – Actions – E-Mail
New resource

## Slide 107: AWS IoT – Actions – E-Mail
New Topic

## Slide 108: AWS IoT – Actions – E-Mail
Subscribe to a topic

## Slide 109: AWS IoT – Actions – E-Mail
Email Notification

## Slide 110: AWS IoT – Actions – E-Mail
Confirm a subscription

## Slide 111: AWS IoT – Actions – E-Mail
Confirm a subscription

## Slide 112: AWS IoT – Actions – E-Mail
New Resource and Role

## Slide 113: AWS IoT – Actions – E-Mail
New Resource and Role

## Slide 114: AWS IoT – Actions – E-Mail
Test

## Slide 115: AWS IoT – Actions – E-Mail
Test

## Slide 116: AWS IoT – Conditional Data Testing

## Slide 117: AWS IoT – Conditional Data Testing

## Slide 118: AWS IoT – Conditional Data Testing

## Slide 119: AWS IoT – Conditional Data Testing

## Slide 120: AWS IoT
Simple Storage Service (S3)

## Slide 121: AWS IoT – S3
Simple Storage Service (S3)

## Slide 122: AWS IoT – S3
Simple Storage Service (S3)

## Slide 123: AWS IoT – S3
Simple Storage Service (S3)

## Slide 124: AWS IoT – S3
Simple Storage Service (S3)

## Slide 125: AWS IoT – S3
Simple Storage Service (S3)

## Slide 126: AWS IoT – S3
Simple Storage Service (S3)

## Slide 127: AWS IoT – S3
Simple Storage Service (S3)

## Slide 128: AWS IoT – S3
Simple Storage Service (S3)

## Slide 129: AWS IoT – S3
Simple Storage Service (S3)

## Slide 130: AWS IoT – S3
Simple Storage Service (S3)

## Slide 131: AWS IoT – S3
Simple Storage Service (S3)

## Slide 132: AWS IoT – Kinesis Firehose
Kinesis Firehose

## Slide 133: AWS IoT – Kinesis Firehose

## Slide 134: AWS IoT – Kinesis Firehose

## Slide 135: AWS IoT – Kinesis Firehose

## Slide 136: AWS IoT – Kinesis Firehose

## Slide 137: AWS IoT – Kinesis Firehose

## Slide 138: AWS IoT – Kinesis Firehose

## Slide 139: AWS IoT – Kinesis Firehose

## Slide 140: AWS IoT – Kinesis Firehose

## Slide 141: AWS IoT – Kinesis Firehose

## Slide 142: AWS IoT – Kinesis Firehose

## Slide 143: AWS IoT – Kinesis Firehose

## Slide 144: AWS IoT – Kinesis Firehose

## Slide 145: AWS IoT – Kinesis Firehose

## Slide 146: AWS IoT – Kinesis Firehose

## Slide 147: AWS IoT – Kinesis Firehose

## Slide 148: AWS IoT – Kinesis Firehose

## Slide 149: AWS IoT – Kinesis Firehose

## Slide 150: AWS IoT – DynamoDB
DynamoDB

## Slide 151: AWS IoT – DynamoDB

## Slide 152: AWS IoT – DynamoDB

## Slide 153: AWS IoT – DynamoDB

## Slide 154: AWS IoT – DynamoDB

## Slide 155: AWS IoT – DynamoDB

## Slide 156: AWS IoT – DynamoDB

## Slide 157: AWS IoT – DynamoDB

## Slide 158: AWS IoT – Data Pipeline
Move data from DynamoDB to S3

## Slide 159: AWS IoT – Data Pipeline
Search for Data Pipeline in services (North Virginia)
Create Pipeline

## Slide 160: AWS IoT – Data Pipeline

## Slide 161: AWS IoT – Data Pipeline

## Slide 162: AWS IoT – Data Pipeline

## Slide 163: AWS IoT – Data Pipeline

## Slide 164: AWS IoT – Glue
Fully managed extract,transform and Load (ETL) service that makes it easy for customers to prepare and load data for analytics

## Slide 165: AWS IoT – Glue

## Slide 166: AWS IoT – Glue Crawl data
Search Glue. Add tables using a crawler

## Slide 167: AWS IoT – Glue Crawl data

## Slide 168: AWS IoT – Glue Crawl data

## Slide 169: AWS IoT – Glue Crawl data

## Slide 170: AWS IoT – Glue Crawl data

## Slide 171: AWS IoT – Glue Crawl data

## Slide 172: AWS IoT – Glue Crawl data

## Slide 173: AWS IoT – Glue Crawl data

## Slide 174: AWS IoT – Glue Crawl data

## Slide 175: AWS IoT – Glue Crawl data

## Slide 176: AWS IoT – Glue Crawl data

## Slide 177: AWS IoT – ETL Jobs

## Slide 178: AWS IoT – ETL Jobs

## Slide 179: AWS IoT – ETL Jobs

## Slide 180: AWS IoT – ETL Jobs

## Slide 181: AWS IoT – ETL Jobs

## Slide 182: AWS IoT – ETL Jobs

## Slide 183: AWS IoT – ETL Jobs

## Slide 184: AWS IoT – ETL Jobs

## Slide 185: AWS IoT – ETL Jobs

## Slide 186: AWS IoT – ETL Jobs

## Slide 187: AWS IoT – ETL Jobs

## Slide 188: AWS IoT – ETL Jobs

## Slide 189: AWS IoT – ETL Jobs

## Slide 190: AWS QuickSight

## Slide 191: AWS QuickSight

## Slide 192: AWS QuickSight

## Slide 193: AWS QuickSight

## Slide 194: AWS QuickSight

## Slide 195: AWS QuickSight

## Slide 196: IoT Data analytics

## Slide 197: IoT Data analytics

## Slide 198: IoT Data analytics

## Slide 199: Thank You
Raghu Prasad
9845547471
www.kaushalya.tech
FB : https://www.facebook.com/raghuprasadkonandur/
Skill Up-Skill Re-Skill
Excellence in action